## Slide 1
Basic Electronics
OP-AMP

## Slide 2: Operational Amplifier
Introduction to operational amplifiers, Op-amp input modes and parameters.
Negative Feedback, Op-amp with negative feedback, Comparators.
Opamp as inverting amplifier

## Slide 3: OP-AMP (operational amplifier)
An OP-AMP is an integrated circuit (IC) used for amplification of signals.
It is the most widely used analog IC.
It is used in control systems, instrumentation, signal processing etc

## Slide 4: Operational Amplifier
The Operational Amplifier or "op-amp" is an amplifier with two inputs and one output. One input is the inverting input and the other is a non inverting input.

## Slide 5: OP-AMP BLOCK DIAGRAM
Figure 1 Op Amp Block Diagram
Inverting Input (- VIN)
+ V
- V
Output
Noninverting Input (+ VIN)
Differential Amplifier
Voltage Amplifier
Output Amplifier

## Slide 6: OP-AMP HAS 3 –STAGE AMPLIFIER CIRCUITS
First Stage : Differential Amplifier -it gives the OP-AMP high input impedance (resistance)
Second Stage: Voltage Amplifier – it gives high gain
Third Stage : Output Amplifier (Emitter Follower) – gives low output impedance (resistance)

## Slide 7: Pin Diagram
Figure 4 Op Amp pins Description
1
2
3
4
5
6
7
8
1. Offset Null
-VEE
8. N / C
6.Output
741
7. +VCC
3. Noninverting Input +VIN
2. Inverting Input –VIN
5.Offset Null

## Slide 8: What are these pins?
Pin 1 and Pin 5 : Offset null input, are used to remove the Offset voltage.
Pin 2: Inverting input (-VIN), signals at this pin will be inverted at output Pin 6.
Pin 3: Non-inverting input (+VIN), signals at pin 3 will be processed without inversion.
Pin 4: Negative power supply terminal (-VEE).
Pin 6: Output (VOUT) of the Op-Amp
Pin 7: Positive power supply terminal (+VCC)
Pin 8: No connection (N\C), it is just there to make it a standard 8-pin

## Slide 9: Symbol of OP-AMP
Figure 5 Op Amp Schematic Symbols
-VIN
+
-
+VIN
VOUT
-VIN
+
-
+VIN
VOUT
+VS
-VS
(a) Without power connection
(b) With power connection

## Slide 10: OP-AMP CONFIGURATIONS
Figure Types of Feedback
(a) No Feedback (open loop comparator circuit)
(b) Negative Feedback
(c) Positive Feedback

## Slide 11: Analyze Yourself
Q1 : Opamp is a ………amplifier.
a) Single Stage
b) Two stage
c) Three Stage or multi stage
d) None of the above
Q2: The supply voltage range of Opamp is…..
a)±5 to ±22V
  b)±7 to ±12V
  c)±12 to ±25V
  d)None of these

## Slide 12: Analyze Yourself
Q3. The voltage measured between the i/p terminals is called….
a)Differential i/p voltage
b)Common mode i/p voltage
c)None of these
Q4. The ideal value of differential gain is……
a)0
b)∞
c)2×105

## Slide 13: Analyze Yourself
Q5. Due to……the ideal OPAMP does not load any source.
a)Ro= 0
b)Av = ∞
c)Ri = ∞
d)CMRR = ∞
Q6. The input offset voltage and input bias current depend on…..
a)RL c)Temperature
b)±Vcc

## Slide 14: Analyze Yourself
Q7. CMRR value indicates the capability to reject……
a)Power supply variations
b)Differential signal
c)Common mode signal
Q8. CMRR is the ratio of….
a)Vc/Vd
b)Vd/Vc
c)Vd/Vcc
d)Ad/Ac

## Slide 15: Analyze Yourself
Q9. The slew rate & bandwidth of an ideal OPAMP are…..&…….
a)0 ,∞
b)∞ ,0
c)∞ ,∞
d)0 ,0
Q10. Ri of an IC741 is……
a)∞
b)Few GΩ
c)2MΩ

## Slide 16: Analyze Yourself
Q11. Ro of an IC741 is……
a)50Ω
b)100Ω
c)75Ω
Q12. The OPAMP should be operated in the…. Region of its transfer characteristics to avoid waveform distortion.
a)Negative saturation
b)Positive saturation
c)Linear

## Slide 17: Feedback
No feedback : Open loop (used in comparators)
Negative feedback : Feedback to the inverting input (Used in amplifiers)
Positive feedback : Feedback to the non inverting input (Used in oscillators(

## Slide 18: OP-AMPS WITH NEGATIVE FEEDBACK
  The two basic amplifier circuits with negative feedback are:
The non-inverting Amplifier.
The inverting Amplifier
(Note: Negative feedback is used to limit the gain)

## Slide 19: NON-INVERTING AMPLIFIER
The input signal is applied to the non-inverting input (+VIN). The output is fed back to the inverting input through resistor RF.
VO
VIN
RF
R1
Figure 11 Closed-Loop Noninverting Amplifier Circuit
Where;
VO = Output voltage
Vin= Input voltage= Vf
ANI = Noninverting Gain

## Slide 20: INVERTING AMPLIFIER
The input signal is applied through a series input resistor RI to the inverting input. Also, the output is fed back through RF to the same input. The noninverting input is grounded.
Where;
VO = Output voltage
VIN = Input voltage
AI = Inverting Gain
VO
VIN
RF
RIN

## Slide 21: Analyze Yourself
Q1.Negative feedback is used by……
a) Oscillators
b) Amplifiers
c)Rectifiers
Q2. Oscillator use……feedback.
a)Positive
b)Negative
c)no

## Slide 22: Analyze Yourself
Q3. A voltage gain of the feedback amplifier is…..
a)Vf/Vout
b)Vout/Vin
c)Vout/Vs
d)Vs/Vf
Q4.The feedback β is……
a)Vf/Vout d)Vs/Vf
b)Vout/Vin
c)Vout/Vs

## Slide 23: Analyze Yourself
Q5. If A = 100 & β = 0.05 what is the value of Af with negative feedback.
a)15
b)16.67
c)600
Q6. According to………concept the two input terminals are at the same potential for the OPAMP.
a)Virtual ground c)Infinite Ro
b)Positive feedback

## Slide 24: Analyze Yourself
Q7. The phase shift between input & output in an inverting amplifier is……
a)0˚ c)90˚
b)180˚ d)270˚
Q8.The gain of the inverting amplifier using Rf = 10kΩ & R1 = 1kΩ is…..
a)-10 c)10
d)11 b)-11

## Slide 25: Analyze Yourself
Q9. The closed loop gain of…….ckt is always greater than 1.
a)Inverting amplifier
b)Voltage follower
c)Non inverting amplifier
Q10. For the amplifier the o/p voltage is…….

## Slide 26: Analyze Yourself
Q11. For the non inverting amplifier Rf = 100kΩ & R1 = 1kΩ then the voltage gain is…..
a)-100 b)101
c)100
Q12. The inverting amplifier ckt has R1 = 1kΩ & Rf = 3kΩ the o/p voltage is……….when Vi = 4V.
a)-6V b)-16V
c)-12V d)-18V

## Slide 27: Analyze Yourself
Q13. _________ feedback is used in a comparator .
a)positive
b)negative
c)no
Q14. For a ckt of fig. Vo = +Vsat for…..
a)Vin < Vref
b)Vin > Vref
c)Vin ≥ Vref

## Slide 28: Analyze Yourself
Q10. The internal resistance divider of 555 generated ……and…..as reference voltages for the internal comparator.
a)Vcc,GND b)5V,-5V c)2/3Vcc, 1/3Vcc
d)None of these
Q11. The expression for on time in the astable mode is….
a)0.693RBC b)0.693RAC
c)0.693 (RA+RB)C d)None of these

## Slide 29: Analyze Yourself
Q12. The duty cycle of the waveform shown in fig. is…..
a)1.5 b)0.6 c)0.4 d)0.67
Q13. Duty cycle of a perfect square wave is….%
a)0 b)100 c)50
Q14. If RA = 1kΩ , RB =1kΩ , C =1µF ,then frequency of an astable multivibrator…..
a)480Hz b)4.8KHz c)48KHz d)48Hz